## Slide 1: Instructions: Language of the Computer
[Adapted from Computer Organization and Design,
Patterson & Hennessy]

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets

## Slide 3: The RISC-V Instruction Set
Used as the example throughout the book
Developed at UC Berkeley as open ISA
Now managed by the RISC-V Foundation (riscv.org)
Typical of many modern ISAs
  See RISC-V Reference Data tear-out card
Similar ISAs have a large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …

## Slide 4: Arithmetic Operations
Add and subtract, three operands
Two sources and one destination
  add a, b, c // a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost

## Slide 5: Arithmetic Example
  C code:
f = (g + h) - (i + j);
  Compiled RISC-V code:
add t0, g, h // temp t0 = g + h add t1, i, j // temp t1 = i + j sub f, t0, t1 // f = t0 - t1

## Slide 6: Register Operands
Arithmetic instructions use register operands
RISC-V has a 32 × 64-bit register file
  Use for frequently accessed data
  64-bit data is called a “doubleword”
  32 x 64-bit general purpose registers x0 to x31
  32-bit data is called a “word”
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations

## Slide 7: RISC-V Registers
  x0: the constant value 0
  x1: return address
  x2: stack pointer
  x3: global pointer
  x4: thread pointer
  x5 – x7, x28 – x31: temporaries
  x8: frame pointer
  x9, x18 – x27: saved registers
  x10 – x11: function arguments/results
  x12 – x17: function arguments

## Slide 8: Register Operand Example
  C code:
f = (g + h) - (i + j);
f, …, j in x19, x20, …, x23
  Compiled RISC-V code:
add x5, x20, x21 add x6, x22, x23 sub x19, x5, x6

## Slide 9: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
RISC-V is Little Endian
  Least-significant byte at least address of a word
  c.f. Big Endian: most-significant byte at least address
RISC-V does not require words to be aligned in memory
  Unlike some other ISAs

## Slide 10: Memory Operand Example
  C code:
A[12] = h + A[8];
h in x21, base address of A in x22
  Compiled RISC-V code:
Index 8 requires offset of 64
8 bytes per doubleword
ld x9, 64(x22) add x9, x21, x9 sd x9, 96(x22)

## Slide 11: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 12: Immediate Operands
  Constant data specified in an instruction
addi x22, x22, 4
  Make the common case fast
Small constants are common
Immediate operand avoids a load instruction

## Slide 13: Unsigned Binary Integers
  Given an n-bit number
  Range: 0 to +2n – 1
  Example
0000 0000 … 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
  Using 64 bits: 0 to +18,446,774,073,709,551,615

## Slide 14: 2s-Complement Signed Integers
  Given an n-bit number
  Range: –2n – 1 to +2n – 1 – 1
  Example
1111 1111 … 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
  Using 64 bits: −9,223,372,036,854,775,808 to 9,223,372,036,854,775,807

## Slide 15: 2s-Complement Signed Integers
Bit 63 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 16: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 0010two
  –2 = 1111 1111 … 1101two + 1 = 1111 1111 … 1110two

## Slide 17: Sign Extension
Representing a number using more bits
  Preserve the numeric value
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110
In RISC-V instruction set
  lb: sign-extend loaded byte
  lbu: zero-extend loaded byte

## Slide 18: Representing Instructions
Instructions are encoded in binary
  Called machine code
RISC-V instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!

## Slide 19: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111

## Slide 20: RISC-V R-format Instructions
Instruction fields
  opcode: operation code
  rd: destination register number
  funct3: 3-bit function code (additional opcode)
  rs1: the first source register number
  rs2: the second source register number
  funct7: 7-bit function code (additional opcode)
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits

## Slide 21: R-format Example
add x9,x20,x21
0000 0001 0101 1010 0000 0100 1011 0011two = 015A04B316
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0
21
20
9
0
51
0000000
10101
10100
01001
000
0110011

## Slide 22: RISC-V I-format Instructions
Immediate arithmetic and load instructions
  rs1: source or base address register number
  immediate: constant operand, or offset added to base address
    2s-complement, sign extended
Design Principle 3: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits

## Slide 23: RISC-V S-format Instructions
Different immediate format for store instructions
  rs1: base address register number
  rs2: source operand register number
  immediate: offset added to base address
    Split so that rs1 and rs2 fields always in the same place
rs2
rs1
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
imm[11:5]
imm[4:0]

## Slide 24: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 25: Logical Operations
Instructions for bitwise manipulation
Useful for extracting and inserting groups of bits in a word

## Slide 26: Shift Operations
immed: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  slli by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srli by i bits divides by 2i (unsigned only)
rs1
rd
funct3
opcode
6 bits
7 bits
5 bits
5 bits
3 bits
funct6
immed
6 bits

## Slide 27: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and x9,x10,x11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x11
x9
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00001100 00000000

## Slide 28: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or x9,x10,x11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x11
x9
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00111101 11000000

## Slide 29: XOR Operations
Differencing operation
  complement some bits, leave others unchanged
xor x9,x10,x12 // NOT operation
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x12
x9
11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
11111111 11111111 11111111 11111111 11111111 11111111 11110010 00111111

## Slide 30: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs1, rs2, L1
  if (rs1 == rs2) branch to instruction labeled L1
bne rs1, rs2, L1
  if (rs1 != rs2) branch to instruction labeled L1

## Slide 31: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in x19, x20, …
Compiled RISC-V code:
bne x22, x23, Else add x19, x20, x21 beq x0,x0,Exit // unconditional Else: sub x19, x20, x21 Exit: …
Assembler calculates addresses

## Slide 32: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in x22, k in x24, address of save in x25
Compiled RISC-V code:
Loop: slli x10, x22, 3 add x10, x10, x25 ld x9, 0(x10) bne x9, x24, Exit
addi x22, x22, 1 beq x0, x0, Loop Exit: …

## Slide 33: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 34: More Conditional Operations
blt rs1, rs2, L1
  if (rs1 < rs2) branch to instruction labeled L1
bge rs1, rs2, L1
  if (rs1 >= rs2) branch to instruction labeled L1
Example
  if (a > b) a += 1;
  a in x22, b in x23
  bge x23, x22, Exit // branch if b >= a
  addi x22, x22, 1
  Exit:

## Slide 35: Signed vs. Unsigned
Signed comparison: blt, bge
Unsigned comparison: bltu, bgeu
Example
  x22 = 1111 1111 1111 1111 1111 1111 1111 1111
  x23 = 0000 0000 0000 0000 0000 0000 0000 0001
  x22 < x23 // signed
    –1 < +1
  x22 > x23 // unsigned
    +4,294,967,295 > +1

## Slide 36: Procedure Calling
Steps required
  Place parameters in registers x10 to x17
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call (address in x1)

## Slide 37: Procedure Call Instructions
Procedure call: jump and link
jal x1, ProcedureLabel
  Address of following instruction put in x1
  Jumps to target address
Procedure return: jump and link register
jalr x0, 0(x1)
  Like jal, but jumps to 0 + address in x1
  Use x0 as rd (x0 cannot be changed)

## Slide 38: Leaf Procedure Example
Procedure that doesn’t call all any other procedures
C code:
long long int leaf_example ( long long int g, long long int h, long long int i, long long int j) { long long int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in x10, …, x13
  f in x20
  temporaries x5, x6
  Need to save x5, x6, x20 on stack

## Slide 39: Leaf Procedure Example
RISC-V code:
leaf_example:
addi sp,sp,-24 Save x5, x6, x20 on stack
sd x5,16(sp)
sd x6,8(sp)
sd x20,0(sp)
add x5,x10,x11 x5 = g + h
add x6,x12,x13 x6 = i + j
sub x20,x5,x6 f = x5 – x6
addi x10,x20,0 copy f to return register
ld x20,0(sp) Resore x5, x6, x20 from stack
ld x6,8(sp)
ld x5,16(sp)
addi sp,sp,24
jalr x0,0(x1) Return to caller

## Slide 40: Local Data on the Stack

## Slide 41: Register Usage
x5 – x7, x28 – x31: temporary registers
  Not preserved by the callee
x8 – x9, x18 – x27: saved registers
  If used, the callee saves and restores them

## Slide 42: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 43: Non-Leaf Procedure Example
C code:
long long int fact (long long int n) { if (n < 1) return 1; else return n * fact(n - 1); }
  Argument n in x10
  Result in x10

## Slide 44: Non-Leaf Procedure Example
RISC-V code:
fact:
addi sp,sp,-16 Save return address and n on stack
sd x1,8(sp)
sd x10,0(sp)
addi x5,x10,-1 x5 = n - 1
bge x5,x0,L1 if n >= 1, go to L1
addi x10,x0,1 Else, set return value to 1
addi sp,sp,16 Pop stack, don’t bother restoring values
jalr x0,0(x1) Return
L1: addi x10,x10,-1 n = n - 1
jal x1,fact call fact(n-1)
addi x6,x10,0 move result of fact(n - 1) to x6
ld x10,0(sp) Restore caller’s n
ld x1,8(sp) Restore caller’s return address
addi sp,sp,16 Pop stack
mul x10,x10,x6 return n * fact(n-1)
jalr x0,0(x1) return

## Slide 45: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  x3 (global pointer) initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage

## Slide 46: Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 47: Byte/Halfword/Word Operations
RISC-V byte/halfword/word load/store
  Load byte/halfword/word: Sign extend to 64 bits in rd
    lb rd, offset(rs1)
    lh rd, offset(rs1)
    lw rd, offset(rs1)
  Load byte/halfword/word unsigned: Zero extend to 64 bits in rd
    lbu rd, offset(rs1)
    lhu rd, offset(rs1)
    lwu rd, offset(rs1)
  Store byte/halfword/word: Store rightmost 8/16/32 bits
    sb rs2, offset(rs1)
    sh rs2, offset(rs1)
    sw rs2, offset(rs1)

## Slide 48: 32-bit Constants
Most constants are small
  12-bit immediate is sufficient
For the occasional 32-bit constant
lui rd, constant
  Copies 20-bit constant to bits [31:12] of rd
  Extends bit 31 to bits [63:32]
  Clears bits [11:0] of rd to 0
lui x19, 976 // 0x003D0
0000 0000 0011 1101 0000
0000 0000 0000 0000
addi x19,x19,1280 // 0x500
0000 0000 0000 0000
0000 0000 0000
0000 0000 0011 1101 0000
0000 0000 0000 0000
0000 0000 0000 0000
0101 0000 0000

## Slide 49: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
SB format:
PC-relative addressing
  Target address = PC + immediate × 2
rs2
rs1
funct3
opcode
imm [10:5]
imm [4:1]
imm[12]
imm[11]

## Slide 50: Jump Addressing
Jump and link (jal) target uses 20-bit immediate for larger range
UJ format:
For long jumps, eg, to 32-bit absolute address
  lui: load address[31:12] to temp register
  jalr: add address[11:0] and jump to target
rd
opcode
7 bits
5 bits
imm[11]
imm[20]
imm[10:1]
imm[19:12]

## Slide 51: RISC-V Addressing Summary

## Slide 52: RISC-V Encoding Summary

## Slide 53: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions

## Slide 54: Synchronization in RISC-V
Load reserved: lr.d rd,(rs1)
  Load from address in rs1 to rd
  Place reservation on memory address
Store conditional: sc.d rd,(rs1),rs2
  Store from rs2 to address in rs1
  Succeeds if location not changed since the lr.d
    Returns 0 in rd
  Fails if location is changed
    Returns non-zero value in rd

## Slide 55: Synchronization in RISC-V
Example 1: atomic swap (to test/set lock variable)
  again: lr.d x10,(x20)
  sc.d x11,(x20),x23 // X11 = status
  bne x11,x0,again // branch if store failed
  addi x23,x10,0 // X23 = loaded value
Example 2: lock
  addi x12,x0,1 // copy locked value
  again: lr.d x10,(x20) // read lock
  bne x10,x0,again // check if it is 0 yet
  sc.d x11,(x20),x12 // attempt to store
  bne x11,x0,again // branch if fails
  Unlock:
  sd x0,0(x20) // free lock

## Slide 56: Translation and Startup
Static linking

## Slide 57: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: described contents of object module
  Text segment: translated instructions
  Static data segment: data allocated for the life of the program
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code

## Slide 58: Linking Object Modules
Produces an executable image
  1. Merges segments
  2. Resolve labels (determine their addresses)
  3. Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space

## Slide 59: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including sp, fp, gp)
  6. Jump to startup routine
    Copies arguments to x10, … and calls main
    When main returns, do exit syscall

## Slide 60: Dynamic Linking
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all (transitively) referenced libraries
  Automatically picks up new library versions

## Slide 61: Starting Java Applications
Interprets bytecodes
Compiles bytecodes of “hot” methods into native code for host machine
Simple portable instruction set for the JVM

## Slide 62: Effect of Compiler Optimization
Compiled with gcc for Pentium 4 under Linux

## Slide 63: Effect of Language and Algorithm

## Slide 64: Lessons Learnt
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
Nothing can fix a dumb algorithm!

## Slide 65: MIPS Instructions
MIPS: commercial predecessor to RISC-V
Similar basic set of instructions
  32-bit instructions
  32 general purpose registers, register 0 is always 0
  32 floating-point registers
  Memory accessed only by load/store instructions
    Consistent use of addressing modes for all data sizes
Different conditional branches
  For <, <=, >, >=
  RISC-V: blt, bge, bltu, bgeu
  MIPS: slt, sltu (set less than, result is 0 or 1)
    Then use beq, bne to complete the branch

## Slide 66: Instruction Encoding

## Slide 67: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less productivity

## Slide 68: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accrete more instructions
x86 instruction set

## Slide 69: Pitfalls
Sequential words are not at sequential addresses
  Increment by 4, not by 1!
Keeping a pointer to an automatic variable after procedure returns
  e.g., passing pointer back via an argument
  Pointer becomes invalid when stack popped

## Slide 70: Concluding Remarks
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Good design demands good compromises
Make the common case fast
Layers of software/hardware
  Compiler, assembler, hardware
RISC-V: typical of RISC ISAs